## Slide 1: Can electrons be local?
Emerging models for local electricity supply and market access
Felix Wight
Commercial Director, Connected Response
Non-exec director, Repowering London
felixwight@connectedresponse.co.uk
Presentation to CEL members
10/9/2025

## Slide 2: Key distinctions
Private network/ public network
Physical/virtual metering
Rural/urban
Domestic/non-domestic
Licensed/license exempt
Metering/settlement
MPAN/meter

## Slide 3: License exemptions
Notes: Even if license exempt, there are practical and administrative challenges to interfacing with the licensed electricity system

## Slide 4: Industry interfaces
Metering- DCC, DCDA
Industry flows- DTN
Industry codes- BSC, SEC, REC, CUSC, DCUSA
Network charges- BSUoS, DUoS, TNUoS, BSC costs
Policy costs- RO, FiT, CfD, WHD, Capacity Market
Other participants- MOPs, Suppliers
Notes: Even if license exempt, there are practical and administrative challenges to interfacing with the licensed electricity system

## Slide 5: Operational requirements
Billing systems
Customer service
Contract management
Procurement
Legal services
Meter installations
Network maintenance
Notes: Even if license exempt, there are practical and administrative challenges to interfacing with the licensed electricity system

## Slide 6: Retail cost breakdown
Component | % of Bill | £ / year (on £1,200 bill) | Cumulative %
Wholesale Energy | 35% | ~£420 | 35%
Network Costs (TNUoS + DUoS + losses) | 23% | ~£276 | 58%
Balancing Costs (BSUoS + imbalance) | 7% | ~£84 | 65%
Environmental & Social Levies | 15% | ~£180 | 80%
Supplier Operating Costs & Margin | 15% | ~£180 | 95%
VAT | 5% | ~£60 | 100%
Notes: Wholesale costs are only 35% of the retail cost

## Slide 7: What is local electricity supply
Notes: Creating direct relationships between demand and generation- physical or commercial
Not all models are technically supply- some involve creating local electricity markets or supply facilitation

## Slide 8
Notes: The big 6 vs the 1.6 million

## Slide 9
M
PUBLIC
PRIVATE

## Slide 10: Local supply models for houses

## Slide 11
M
PUBLIC
PRIVATE

## Slide 12
M
PUBLIC
PRIVATE
License exempt generation:20kWh
License exempt demand:20kWh
Licensed import:10kWh
-15
-10
-5
+20
-10

## Slide 13
M
PRIVATE
PRIVATE
PRIVATE
PRIVATE
PUBLIC
PUBLIC
PUBLIC
PUBLIC

## Slide 14: BSC Modification P441
Raised by Green Energy UK on behalf of Energy Local in July 2022
‘Minded to’ position agreed in June 2025
Public consultation expected September 2025
Provides clarity on network charges relating to ‘complex’ metering arrangements
Requires half hourly metering data
Not all households need to sign up
Applicable to domestic and non-domestic customers
Technically limited to demand and generation behind same primary or secondary substation
Notes: Energy Local

## Slide 15
License exempt generation:20kWh
License exempt demand:20kWh
Licensed import:10kWh
VIRTUAL METER
+20
-15
-5
-10

## Slide 16: Local supply models for flats

## Slide 17: Private wire- solar splitting
Static or dynamic splitting of communal solar
Requires physical connection from solar inverter to flat for connection ‘behind the meter’
Provides access to solar independently of choice of supplier
Solar usage billed separately from grid electricity
Can provide improvement to flat EPC rating
Operational example: Solshare

## Slide 18: Private wire- communal meter
Physical ‘boundary’ meter measures total import and export from the block
Flats typically have new sub-meters fitted to measure individual consumption (replacing existing smart meter in retrofit scenario)
Solar and grid electricity can be billed separately or combined
Can be more difficult for customers to change supplier as all supply is via the communal meter
Operational example: Emergent Energy

## Slide 19: Virtual meter
Virtual meter measures total import and export from participating customers on a half hourly basis
Existing SMETS smart meters can be used
Solar and grid electricity can be billed separately or combined
Requires a licensed supplier to provide billing services and ‘top up’ grid electricity
Operational example: Energy Local Roupell Park
Virtual meter

## Slide 20: BSC Modification P455
Raised by Emergent Energy in June 2023
Implemented September 2024
Allows data from sub-meters on private wire networks to be used for settlement
Simplifies the industry interfaces required for supply on private wire networks
Domestic and Non-domestic

## Slide 21: Non-domestic local supply models

## Slide 22
Notes: Non-domestic on-site generation

## Slide 23
M
PUBLIC
PRIVATE

## Slide 24
PUBLIC
M
PRIVATE

## Slide 25
M
PRIVATE
PUBLIC
M
PRIVATE

## Slide 26: BSC Modification P442
Raised by Urban Chain in July 2022
Implemented February 2025
Creates new role of ‘Exempt Supply Notification Agent’
Enables license exempt generation to recover policy and network costs through a credit mechanism
Non-domestic (currently)
Not limited by distance

## Slide 27: Risks to consider
Operating costs
Customer recruitment
Network maintenance
Meter requirements
Volatility in wholesale costs
Changes to regulation of license exempt supply
Changes to BSC
Notes: Make sure you respond to the P441 consultation

## Slide 28: Opportunities
Adding value to existing installations
New build developments
Shop around for P442 PPA options (Renewable Exchange Urban Chain, PPAYA, Tem)
Forthcoming P441 consultation
Notes: Make sure you respond to the P441 consultation